### Comparative Understanding
#### 1. DIMFMT (Data Format)
- 3D Configuration (DIMFMT = __SE_DIMFMT_3D):
  - Specifies that the data will be interpreted as 3D.
  - The array has three dimensions: COL (columns), ROW (rows), and CHANNEL (channels).
  - This is the most complex structure because you're working with 3 dimensions, and the data is accessed in 3D space.
- 2D Configuration (DIMFMT = __SE_DIMFMT_2D):
  - Specifies that the data will be interpreted as 2D.
  - The array has only two dimensions: COL (columns) and ROW (rows).
  - The data is accessed in two-dimensional space.
Key Difference:
In the 3D configuration, you need a third dimension (CHANNEL), whereas in the 2D configuration, you have only rows and columns (no third dimension).

#### 2. ELETYPE (Element Type)
- 3D Configuration (ELETYPE = __SE_ELETYPE_32BIT):
  - Each element in your array is 32 bits (could be 32-bit integers or floating-point numbers).
  - This means each data entry in the 3D array is represented by 32 bits, which affects memory usage and access speed.
- 2D Configuration (ELETYPE = __SE_ELETYPE_16BIT):
  - Each element in your array is 16 bits (could be 16-bit integers or floating-point numbers).
  - This uses less memory per element, and may be used for smaller or more compact data.
Key Difference:
The 3D configuration uses 32-bit elements, while the 2D configuration uses 16-bit elements. This implies that 3D data takes up more memory per element than 2D data.

#### 3. VECLEN (Vector Length)
- 3D Configuration (VECLEN = __SE_VECLEN_16ELEMS):
  - The system processes 16 elements at a time in a vector, which can be more efficient for memory access and computation.
  - This setting is often used for optimization in hardware or specialized computations.
- 2D Configuration (VECLEN = __SE_VECLEN_16ELEMS):
  - Similarly, the system processes 16 elements at a time in a vector.
  - The VECLEN value doesn't change for both 2D and 3D configurations because it's just an optimization level for processing data in chunks.
Key Difference:
There's no difference in VECLEN between the 2D and 3D configurations in your example. Both process 16 elements per vector. The primary difference is in the dimensions of the data structure, not how elements are grouped for processing.

#### 4. ICNT0, ICNT1, and ICNT2 (Dimension Counters)
These parameters define the size of each dimension in the data structure.
- 3D Configuration:
  - ICNT0 = COL: The number of columns in the first dimension of the array.
  - ICNT1 = ROW: The number of rows in the second dimension.
  - ICNT2 = CHANNEL: The number of channels in the third dimension (this is what makes it 3D).
- 2D Configuration:
  - ICNT0 = COL: The number of columns in the first dimension.
  - ICNT1 = ROW: The number of rows in the second dimension.
  - ICNT2 = 1: There’s no third dimension, so this is set to 1.
Key Difference:
- For 3D, you set ICNT2 = CHANNEL, which introduces the third dimension (channels).
- For 2D, there is no third dimension, so you set ICNT2 = 1 to indicate the absence of a third dimension.

#### 5. DIM1, DIM2 (Dimension Sizes)
These parameters represent the total number of elements in each dimension.
- 3D Configuration:
  - DIM1 = COL: The first dimension (COL) represents the number of elements in each row of the 3D array.
  - DIM2 = CHANNEL * ROW: The second dimension is the product of ROW and CHANNEL, which represents the total number of elements in the second dimension. This accounts for both rows and channels.
- 2D Configuration:
  - DIM1 = COL: Same as in the 3D configuration, it represents the number of elements in each row.
  - DIM2 = 0: Since there's no third dimension in 2D, DIM2 is set to 0 to indicate that the second dimension is only defined by the rows and columns.
Key Difference:
- In the 3D configuration, DIM2 accounts for the interaction between ROW and CHANNEL.
- In the 2D configuration, DIM2 is set to 0 since there’s no third dimension.